## Slide 1: sanos
Server Appliance Network Operating System
Tehnical Overview
Copyright (C) 2002 Michael Ringgaard, All rights reserved.

## Slide 2: SanOS Features 1
No nonsense modern application server operating system kernel.
Runs on standard PC hardware.
Simple installation.
32-bit protected mode.
Interrupt driven.
Multi tasking.
Single address space.
Kernel protection.
Virtual memory.
PE dynamically loadable modules (standard EXE/DLL format).
Both kernel and user modules.
Low memory footprint (less than 512 KB RAM)
Lightweight
Embedding support with PC104 and Flash devices

## Slide 3: SanOS Features 2
Self configuring (PCI & PnP support)
TCP/IP networking stack
Very efficient multithreading
High performance and stability through simplicity.
Written in C (98%) and x86 assembler (2%)
Development using Microsoft Visual C.
Remote source level debugging support (windbg)

## Slide 4: Hardware
Standard PC architecture
IA-32 processor (486, Pentium)
RAM (min. 4 MB)
IDE disk (UDMA)
Standard floppy
Serial ports
Keyboard
Video controller
NIC support:
  Novell NE2000
  AMD PCNET32
  3COM 3C905
  ...

## Slide 5: Core Operating System Services
System booting and application loading
Memory Management
  Virtual memory mapping
  Physical memory allocation and paging
  Heap allocation and module loading and linking
Thread Control Management
  Thread scheduling
  Thread context
  Thread synchronizarion
I/O Management
  Block devices and filesystems
  Stream devices
  Packet devices (NIC) and networking (TCP/IP)

## Slide 6: Overview
Part 1: Architecture
Part 2: Boot Process
Part 3: Memory Management
Part 4: Thread Control
Part 5: I/O Management

## Slide 7: Part 1
Architecture

## Slide 8: Virtual Address Space Layout
Virtual address space divided into kernel region and user region.
Ring 0 code (kernel) can access all 4 GB.
Ring 3 code (user) can only access low 2 GB addess space.
Kernel and user segment selectors controls access to address space.
kernel
user
0x80000000
0x00010000
0xFFFFFFFF
0x00000000
invalid
user space
(2 GB)
kernel space
(2 GB)

## Slide 9: Segment selectors
Name | GDT index | Base | Limit | Access
NULL | 0 | 0x00000000 | 0x00000000 | None
KTEXT | 1 | 0x00000000 | 0xFFFFFFFF | Ring 0 CODE
KDATA | 2 | 0x00000000 | 0xFFFFFFFF | Ring 0 DATA
UTEXT | 3 | 0x00000000 | 0x7FFFFFFF | Ring 3 CODE
UDATA | 4 | 0x00000000 | 0x7FFFFFFF | Ring 3 DATA
TSS | 5 |  |  | Ring 0 TSS
TIB | 6 |  |  | Ring 3 DATA
Mode | CS | DS | ES | SS | FS
kernel | KTEXT | KDATA | KDATA | KDATA | TIB
user | UTEXT | UDATA | UDATA | UDATA | TIB

## Slide 10: Kernel Address Space Layout
kernel heap
handle table
page frame database
kernel modules
syspages
0x90800000
0x90400000
0x90000000
0xFFFFFFFF
0x80000000
krnl.dll
page tables
0x91000000
0x92000000
syspage
page directory
video buffer
kmodmap
osvmap
initial tcb
dma buffers
biosdata
bootparams
idt
gdt
tss
data
code
devtab
devicetab
bindtab
intrtab
ready_queue
buckets
kmods
...
invalid
user space
(2 GB)
kernel space
(2 GB)

## Slide 11: User Address Space Layout
peb
os.dll
invalid
initial tib
user space
0x7FFDF000
0x7FF00000
0x00010000
0x80000000
0x00000000
heap
invalid
user space
(2 GB)
kernel space
(2 GB)

## Slide 12: System components
application modules
os.dll
kernel modules and drivers
krnl.dll
osldr.dll
boot
User mode
Kernel mode
Bootstrap

## Slide 13: Kernel Architecture
io
memory
thread
boot
hw
api
cpu
fpu
iop
pit
pic
buf
sched
dbg
start
pframe
pdir
ldr
kmem
vmm
kmalloc
vfs
socket
udpsock
tcpsock
dfs
devfs
trap
dev
ether
netif
loopif
udp
tcp
ip
arp
icmp
dhcp
syscall
pci
pnp
ide
fd
serial
console
kbd
video
pcnet32
ne2000
3c905c
block
stream
packet
bus
(smbfs)
queue
ramdisk
null
cmos
(scsi)
(nic...)
timer
object

## Slide 14: Part 2
Boot Process

## Slide 15: Boot process
BIOS initialization and loading of boot sector.
Boot sector loads bootstrap loader (boot.asm).
Bootstrap loader sets up memory and loads kernel (osldr.dll).
Kernel initializes subsystems and starts main task (krnl.dll).
Main kernel task loads device drivers, mounts filesystems and loads os.dll into user space.
Usermode component (os.dll) initializes user module database, memory heap, and loads and executes the init application (e.g. sh.exe or jinit.exe).
All systems are GO. We are up and running.

## Slide 16: Step 1: BIOS
CPU reset starts executing of ROM BIOS.
BIOS initializes and configures computer and devices.
BIOS loads the boot sector from sector 0 of the boot device (512 bytes) at 0x7C00.
The BIOS jumps to 0:7C00 in 16 bit real-mode.
Partitioned boot devices first loads the master boot record (mbr), which then loads and starts the boot sector in the active boot partition.
BIOS data area
osldr
0x000A0000
0x00010000
memend
0x00000000
BIOS ROM area
boot sector
0x00007C00
boot stack
0x00090000
0x00100000
heap

## Slide 17: Step 2: Boot sector (boot)
Loads the osldr from boot device using BIOS INT 13 services.
Disables interrupts. Interrupts are reenabled when the kernel has been initialized.
Enables A20.
Loads boot descriptors (GDT, IDT).
Initialize segment registers using boot descriptors.
Switches the processor to protected mode.
Calls entry point in osldr.

## Slide 18: Step 3: Bootstrap loader (osldr.dll)
Determines memory size.
Heap allocation starts at 1MB.
Allocate page for page directory.
Make recursive entry for access to pagetables.
Allocate system page.
Allocate initial thread control block (TCB).
Allocate system page directory page.
Map system page, page directory, video buffer, and initial TCB.
Temporarily map first 4MB to physical memory.
Load kernel from boot disk.
Set page directory (CR3) enable paging (PG bit in CR0).
Setup descriptors in syspage (GDT, LDT, IDT and TSS).
Copy boot parameters to syspage.
Reload segment registers.
Switch to initial kernel stack and jump to kernel.

## Slide 19: Step 4: Kernel startup (krnl.dll)
Initialize memory management subsystem
  Initialize page frame database.
  Initialize page directory.
  Initialize kernel heap.
  Initialize kernel allocator.
  Initialize virtual memory manager.
Initialize thread control subsystem
  Initialize interrupts, floating-point, and real-time clock.
  Initialize scheduler.
  Enable interrupts
Start main task
Process idle tasks

## Slide 20: Step 5: Main kernel task (krnl.dll)
Enumerate root host buses and units
Initialize boot devices (floppy and harddisk).
Initialize built-in filesystems (dfs and devfs).
Mount root device.
Load kernel configuration (/etc/krnl.ini).
Initialize kernel module loader.
Load kernel modules.
Bind, load and initialize device drivers.
Initialize networking.
Mount additional filesystems.
Allocate handles for stdin, stdout and stderr.
Allocate and initialize process environment block (PEB).
Load /os/os.dll into user space
Initialize initial user thread (stack and tib)
Call entry point in os.dll

## Slide 21: Step 6: User mode startup (os.dll)
Load user mode selectors into segment registers
Load os configuration (/etc/os.ini).
Initialize heap allocator.
Initialize user module database.
Load, bind and execute initial application.

## Slide 22: Step 7: Execute application
All system are now up and running.
The application uses the OS API, exported from os.dll to call system services.
Examples: sh.exe and jinit.exe
OS API categories:
system
file
network
virtual memory
heap
modules
time
threads
synchronization
critical sections
thread local storage

## Slide 23: OS API Functions
accept
beginthread
bind
calloc
canonicalize
chsize
clock
close
connect
csfree
dbgbreak
dup
endthread
enter
epulse
ereset
eset
exec
exit
flush
format
free
fstat
fstatfs
futime
getcontext
getfsstat
getmodpath
getmodule
getpeername
getprio
getsockname
getsockopt
gettib
gettid
gettimeofday
ioctrl
leave
link
listen
load
lseek
malloc
mkcs
mkdir
mkevent
mksem
mlock
mmap
mount
mprotect
mremap
munlock
munmap
open
opendir
panic
read
readdir
realloc
recv
recvfrom
rename
resolve
resume
rmdir
self
semrel
send
sendto
setcontext
setprio
setsockopt
settimeofday
shutdown
sleep
socket
stat
statfs
suspend
syscall
syslog
tell
time
time
tlsalloc
tlsfree
tlsset
tlsset
unlink
unload
unmount
utime
wait
write

## Slide 24: Win32 subsystem
Partial implementation of the following Win32 modules:
  KERNEL32
  USER32
  ADVAPI32
  MSVCRT
  WINMM
  WSOCK32

## Slide 25: Java VM
SanOS supports any standard pure Java server applications.
Uses Sun Mirosystems Hotspot Java VM for Win32.
Supports standard JNI for native interface.
jinit.exe loads the Java VM and starts the main method of the startup class.
krnl.dll
os.dll
win32 subsys
jinit
jvm
Java server application
(e.g. tomcat, jboss)
(jni)
Java 2 SDK
hpi

## Slide 26: Part 3
Memory Management

## Slide 27: Memory management
pdir.c controls the virtual memory mapping (pdir and ptab).
pframe.c controls the allocation of physical memory (pfdb).
kmem.c tracks the use of the kernel module and heap areas and allocation and mapping of physical pages to virtual addresses (osvmap and kmodmap).
kmalloc.c allocates and deallocates small blocks (<4K) from the kernel heap (buckets). Larger blocks are delegated to kmem.
vmm.c reserves virtual addresses in user space and commits and maps these to physical memory (vmap).
heap.c is a standard C heap allocator (malloc, free, realloc) (Doug Lea) on top of the vmm.
pframe.c
pdir.c
kmem.c
kmalloc.c
vmm.c
heap.c

## Slide 28: Module Loader

## Slide 29: Part 4
Thread Control

## Slide 30: Thread control blocks
esp
thread object
kernel stack
Thread control blocks
Each thread has an 8K thread control block (tcb).
Each tcb is aligned on 8K boundary
tcbs are allocated on the kernel heap.
Initial kernel thread is allocated in syspage block.
esp0 in tss points to stack top in current tcb
tss
esp0

## Slide 31: Thread information block (tib)
esp
thread object
kernel stack
Each user mode thread has a 4K thread information block (tib) allocated in user space.
The format of the tib is compatible with win32.
The fs segment register always references the tib for the current thread.
The tib contains the thread local storage array for the thread.
The tcb contains a reference to the tib for user mode threads.
tib
tls array
fs

## Slide 32: User stacks
esp
thread object
kernel stack
Each user thread has a user mode stack
The first page of the stack is committed when it is created.
The rest of the pages in the stack is reserved with guard pages.
When the stack grows the guard page handler expands down the stack and commits pages.
tib
reserved
stacktop
stacklimit
stackbase
committed
user stack

## Slide 33: Enter kernel (1)
trap/fault occurs (int, exception, interrupt)
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code

## Slide 34: Enter kernel (2)
trap/fault occurs (int, exception, interrupt)
  push user esp on to kernel stack, load kernel esp
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ess
esp

## Slide 35: Enter kernel (3)
trap/fault occurs (int, exception, interrupt)
  push user esp on to kernel stack, load kernel esp
  push user eflags, reset flags (IF=0, TF=0)
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ess
esp
flg

## Slide 36: Enter kernel (4)
trap/fault occurs (int, exception, interrupt)
  push user esp on to kernel stack, load kernel esp
  push user eflags, reset flags (IF=0, TF=0)
  push user eip, load kernel entry eip
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ss
esp
flg
Hardware programmed
single instrution
cs
eip

## Slide 37: Enter kernel (5)
trap/fault occurs (int, exception, interrupt)
  push user esp on to kernel stack, load kernel esp
  push user eflags, reset flags (IF=0, TF=0)
  push user eip, load kernel entry eip
push error code
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ss
esp
flg
Hardware programmed
single instrution
cs
eip
err

## Slide 38: Enter kernel (6)
trap/fault occurs (int, exception, interrupt)
  push user esp on to kernel stack, load kernel esp
  push user eflags, reset flags (IF=0, TF=0)
  push user eip, load kernel entry eip
push error code
push trap number, register and set thread context pointer
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ss
esp
flg
Hardware programmed
single instrution
cs
eip
err
regs
num

## Slide 39: Context record
Context record is a pointer into the kernel stack
This record can be modified while in kernel mode
Context record will be restored when the thread leaves the kernel
tcb
esp0
ss
esp
flg
cs
eip
err
regs
num
context record
struct context
{
unsigned long es, ds;
unsigned long edi, esi, ebp, ebx, edx, ecx, eax;
unsigned long traptype;
unsigned long errcode;
unsigned long eip, ecs;
unsigned long eflags;
unsigned long esp, ess;
};

## Slide 40: Current thread
tcbs are aligned on 8K boundary
The current thread can be obtained from the value of the stack pointer in kernel mode.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
mov ebx, esp
and ebx, -sizeof tcb

## Slide 41: Context switch (1)
Dispatcher calls context_switch to change context to another thread.
Caller pushes new tcb and return address on stack.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
esp
tcb
kernel code
esp
tcb
eip

## Slide 42: Context switch (2)
Dispatcher calls context_switch to change context to another thread.
Caller pushes new tcb and return address on stack.
Registers are saved on current kernel stack.
Store kernel stack pointer in tcb.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
esp
tcb
kernel code
esp
eip
ebp
esi
edi
ebx
tcb

## Slide 43: Context switch (3)
Dispatcher calls context_switch to change context to another thread.
Caller pushes new tcb and return address on stack.
Registers are saved on current kernel stack.
Store kernel stack pointer in tcb.
Fetch stack pointer for new thread and store in esp0.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
esp
tcb
kernel code
esp
eip
ebp
esi
edi
ebx
kernel stack
eip
ebp
esi
edi
ebx
tcb
tcb

## Slide 44: Context switch (4)
Dispatcher calls context_switch to change context to another thread.
Caller pushes new tcb and return address on stack.
Registers are saved on current kernel stack.
Store kernel stack pointer in tcb.
Fetch stack pointer for new thread and store in esp0.
Restore register from new kernel stack.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
esp
tcb
kernel code
esp
eip
ebp
esi
edi
ebx
kernel stack
eip
tcb
tcb

## Slide 45: Context switch (5)
Dispatcher calls context_switch to change context to another thread.
Caller pushes new tcb and return address on stack.
Registers are saved on current kernel stack.
Store kernel stack pointer in tcb.
Fetch stack pointer for new thread and store in esp0.
Restore register from new kernel stack.
Return from context_switch restores eip.
tcb
esp0
kernel stack
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
esp
tcb
kernel code
esp
eip
ebp
esi
edi
ebx
kernel stack
tcb

## Slide 46: System calls (1)
System calls are exported from os.dll.
All kernel system calls are handled by the syscall() function.
When a kernel system call is invoked a privilege transition from user mode to kernel mode takes place, and the stack is switched from user stack to kernel stack.
When the function returns these actions are reversed, the thread switches back to the user stack and returns to user mode privileges.
Consider the system call function(param1, param2). Prior to this function being called, two parameters are pushed onto the user stack in reverse order.
When function() is invoked, the return address is first pushed onto the user stack and then the old base pointer for the previous stack frame is pushed. The call stack after the call looks like:
param2
param1
ret addr
ebp

## Slide 47: System calls (2)
The implementation for function() is as follows: int function(param1, param2) { return syscall(SYSCALL_FUNCTION, &param1); }
syscall() takes two parameters, a system call number, syscallno, and a pointer to the first parameter supplied to the function that calls syscall(). When syscall() is invoked, these two parameters are pushed onto the user stack in reverse order. The return address is pushed onto the stack when the call is made and the first action of the syscall() function is to push the base pointer onto the user stack.
syscall() is an assembly language routine that causes a trap to the kernel through INT 48.
Before doing this, it stores the system call number and pointer to the first parameter of the specific system call in the eax and edx registers, respectively.
param2
param1
ret addr
ebp
syscallno
ret addr
ebp
syscall:
push ebp
mov ebp, esp
mov eax, 8[ebp]
mov edx, 12[ebp]
int 48
leave
ret

## Slide 48: System calls (3)
When the trap is executed the system switches to kernel mode and executes the systrap routine
systrap saves the data segments and takes the two parameters in eax and edx and passes these to the kernel mode syscall routine.
The system trap mechanism has been carefully designed to minimize the number of registers that must be preserved between system calls.
Support for sysenter/sysexit for Pentium processors.
esp
eip
eflags
eax ebx
ecx edx
ebp esi edi
tcb
esp0
user stack
user code
kernel code
ss
esp
flg
cs
eip
ds
params
es
syscallno
systrap:
push ds
push es
push edx
push eax
mov ax, SEL_KDATA
mov ds, ax
mov es, ax
call syscall
add esp, 8
pop es
pop ds
iretd

## Slide 49: Thread states
Threads are created in INITIALIZED state.
When mark_thread_ready() is called the thread moves to the READY state and is inserted into one of the wait queues.
When the scheduler selects the thread for execution it moves to the RUNNING state and the dispatcher swicthes to the processor to the threads context.
The thread continues running until it must wait on an object to become signaled. The thread is added to the waitlist for the object and enters the WAITING state.
When the object is signaled the thread is scheduled for execution by inserting it into the ready queue for the threads priority. The thread enters the READY state.
When the thread terminates it enters the TERMINATED state. The thread object is not removed until all handles to it has been closed.
INITIALIZED
READY
TERMINATED
WAITING
RUNNING

## Slide 50: Scheduling
Threads that are ready to run are scheduled in a round-robin manner based based on priority.
A thread is not scheduled until no higher priority threads are ready to run.
The scheduler has one ready queue for each priority level.
7
highest priority
lowest priority
6
5
4
3
2
1
0
thread
thread
thread
thread
thread

## Slide 51: Synchronization objects
Object types
  THREAD
  EVENT
  TIMER
  MUTEX
  SEMAPHORE
  FILE

## Slide 52: Thread synchronization
The object header contains the object type, signaled state, and a list of the threads waiting on the object.
The waitblock represents a thread waiting on an object.
Each thread has a list of the objects it is waiting on.
thread 1
wait list
thread 2
wait list
object a
waitlist
object b
waitlist
waitblock
next
thread
object
waiter links
waitblock
next
thread
object
waiter links
waitblock
next
thread
object
waiter links

## Slide 53: Part 5
I/O Management

## Slide 54: I/O Components
Device Drivers
Device Manager
Virtual File System layer and filesystems
Socket interface and networking

## Slide 55: Device types
Bus device (enumerate)
  pci
  isapnp
Block device (read, write)
  fd
  hd
Stream device (read, write)
  console
  serial
Packet device (receive, transmit)
  3c905c
  ne2000
  pcnet32

## Slide 56: Filesystems
Virtual File System (vfs)
Filesystems
  dfs
  devfs
  (smbfs)
Buffer Cache Manager

## Slide 57: Networking
Socket interface
Network interface
Protocols
  TCP
  UDP
  IP
  ICMP
  DHCP
  ARP
  IEEE 802.3 (Ethernet)

## Slide 58: Design Principles
Performance
Flexibility
Simplicity